## Slide 1: Switchbox Router Implementation
A Comprehensive Study on Greedy and Conflict Resolution Routing Algorithms
Dhruvil Patel(21JE0312),Dhruv Pathak(21JE0311),Sidhhartha Gaur(21JE0919),Jash Shah(21JE0858)

## Slide 2: Abstract
Evaluation of two switchbox routing methods: greedy and conflict resolution.
Aims to enhance understanding and gain practical experience through implementation.
Focuses on area utilization, wirelength, and via minimization.

## Slide 3: Introduction
Switchbox routing involves connecting pins in a rectangular grid.
Challenge lies in avoiding interference and optimizing routing paths.
This study compares greedy and conflict resolution methods.

## Slide 4: Switchbox Routing Basics
Switchbox: Rectangular region with pins on all four edges.
Routing involves connecting pins belonging to the same net.
Input: Pin locations and associated nets; Output: Routing solution.

## Slide 5: Challenges in Switchbox Routing
NP-complete nature makes finding optimal solutions infeasible.
High pin density increases complexity.
Evaluating routing algorithms involves metrics like area usage and wirelength.

## Slide 6: Greedy Algorithm - Overview
Prioritizes local optimization for quick solutions.
Executes a single pass across the switchbox.
Expands the switchbox as needed to complete routing.

## Slide 7: Greedy Algorithm - Workflow
1. Connect left-side pins to available tracks.
2. Sweep columns left to right, connecting top/bottom pins.
3. Distribute nets with multiple right-side pins progressively.
4. Add columns to resolve unjoined nets.

## Slide 8: Greedy Algorithm - Strengths and Weaknesses
Strengths: Simplicity, speed, and minimal computational effort.
Weaknesses: Lack of global awareness, leading to inefficiencies and poor routing decisions.

## Slide 9: Conflict Resolution Approach - Overview
Focuses on resolving conflicts between nets.
Initial routing places wires without avoiding overlaps.
Conflicts are resolved iteratively by adjusting wire placements.

## Slide 10: Conflict Resolution - Key Steps
1. Initial routing connects all pins, allowing overlaps.
2. Identify conflicts: segment conflicts and via conflicts.
3. Iterative sweeps to resolve conflicts by pushing segments.
4. Increase switchbox size if conflicts persist.

## Slide 11: Conflict Resolution - Strengths and Challenges
Strengths: Effective for complex layouts with higher pin density.
Challenges: High computational complexity and inefficiencies in cleanup processes.

## Slide 12: Comparative Analysis
Greedy Algorithm: Quick but limited in quality for complex layouts.
Conflict Resolution: Superior in larger benchmarks but requires refinement.
Performance evaluated based on area utilization, wirelength, and via minimization.

## Slide 13: Applications - Benchmarks
Tested on Burstein's Difficult Switchbox and Deutsch's Difficult Channel.
Greedy method excelled in simple scenarios.
Conflict resolution demonstrated potential for complex cases with further refinement.

## Slide 14
Comparisons

## Slide 15: Results Summary
Greedy algorithm: Suitable for basic layouts with quick solutions.
Conflict resolution: Better for larger benchmarks but underperforms in extreme cases.
Potential for improvement through enhanced cleanup and via minimization.

## Slide 16: Conclusion
Comparison highlights strengths and limitations of both algorithms.
Greedy router: Efficient for simpler layouts.
Conflict resolution: Promising with further refinement.
Future work includes enhancing cleanup subroutines and minimizing vias.

## Slide 17: References
1. W.K. Luk, 'A greedy switch-box router.'
2. Sabih H. Gerez, 'PACKER: A switchbox router based on conflict elimination.'
3. Additional references as listed in the report.